## Slide 1: CONDENSATION BASED FINITE ELEMENT MODEL REDUCTION STRATEGY FOR STRUCTURAL OPTIMIZATION PROBLEMS
KAKADE Ishaan
CONIGLIO Simone | MORLIER Joseph

## Slide 2: INTRODUCTION

## Slide 3: INTRODUCTION
Figure 1: Finite Element Model of Engine an Pylon
Figure 2: Representative Finite Element Model

## Slide 4: THE BIG PICTURE

## Slide 5: THE BIG PICTURE
During topological optimization processes we use the whole finite element model as our design space (all nodes or degrees of freedom)
We would like to reduce that number to a large extent.
Notes: Primary Goal: The overall goal of this project is to establish a strategy to reduce the complexity of a finite element problem used for optimization purposes by the use of some (or a combination) of reduction strategies to suppress some degrees of freedom while maintaining the full response.
Secondary Goal: Perhaps an additional goal of the project could be to homogenize the material properties of a structure given that more and more aerospace structures now use composite materials with highly discretized material properties across geometries.

## Slide 6: THE BIG PICTURE
Primary Goal: Establish a strategy to reduce the complexity of a finite element problem used for optimization purposes by the use of some (or a combination) of reduction strategies to suppress some degrees of freedom while maintaining the full response – prediction of those degrees of freedom that have been retained.

## Slide 7: THE BIG PICTURE
Secondary Goal: Perhaps an additional goal of the project could be to homogenize the material properties of a structure given that more and more aerospace structures now use composite materials with highly discretized material properties across geometries.
L.D. Flippen Jr, (1994), A Theory of Condensation Model Reduction, Computers Math. Application, Vol. 27 (No. 2), pp. 9 - 40.

## Slide 8: PROBLEM DEFINITION

## Slide 9: PROBLEM DEFINITION
Variable Engine Thickness Architecture
Using Static and Dynamic Condensation Using Varying Techniques
Time Complexity Analysis
Dynamic condensation for Modal Behavior

## Slide 10: PROJECT GOALS

## Slide 11: PROJECT GOALS
1. Integration of A and I as MMA decision variables (for the complete beam truss and by set i.e. vertical and horizontal beams separately).
2. Implement the classical condensation and a new condensation strategy to reduce the number of degrees of freedom of the non-design zone.
3. Comparison of 3 approaches with respect to time complexity.
4. Implementation of dynamic condensation.

## Slide 12: BACKGROUND AND LITERATURE REVIEW

## Slide 13: MODIFIED SIMP APPROACH
Minimise:
Subject to:
where E0 is the stiffness of the material, Emin is a very small stiffness assigned to void regions in order to prevent the stiffness matrix from becoming singular, and p is penalization factor (typically p = 3) introduced to ensure black-and-white solutions. Equation (1) corresponds to the modified SIMP approach, which differs from the classical SIMP approach used in the original paper in the occurrence of the term Emin.

## Slide 14: METHOD OF MOVING ASYMPTOTES
Minimise:
Subject to:
Here, x1… xn are the “true” optimization variables, while y1, …, ym and z are “artificial” optimization variables; f0 f1… fm are given, continuously differentiable, real-valued functions and constitute the constraint functions evaluated at the current values of the variable x; xmin and xmax are given real numbers which satisfy xminj < xmaxj; a0 and ai are given real numbers which satisfy a0 > 0 and ai ≥ 0; ci and di are given real numbers which satisfy ci ≥ 0, di ≥ 0 and ci + di > 0.

## Slide 15: STATIC CONDENSATION
Assume that those secondary degrees of freedom to be reduced or condensed are arranged in the first ‘s’ nodal coordinates and the remaining primary degrees of freedom are the last ‘p’ nodal coordinates.
Where K’ and F’ are the condensed stiffness and force vectors and {u}p is the vector of primary displacement

## Slide 16: DYNAMIC CONDENSATION
Used to include inertia effects in a condensation model
Essentially, a mass re-distribution
Reduction of the Mass Matrix
Guyan condensation

## Slide 17: CONDENSATION
Condensation
Dongsheng Li, Discussion of Model Reduction and Reservation, Procedia Engineering, Volume 188, 2017, Pages 354-361, ISSN 1877-7058,
Figure 3: Spring – Mass System with a certain dynamic and Static Behaviour

## Slide 18: MATLAB IMPLEMENTATION
Figure 4: Function Call Flow Chart on MATLAB

## Slide 19: STATE OF WORK

## Slide 20: OPTIMIZATION PROBLEM
Minimise:
Subject to:
Minimise:
Subject to:
Notes: Where, from the general MMA optimization problem description: a0 = 1, ai = 0, di = 0 and ci = “large number”. The reason ci is large is because we force the variable yi to be “expensive” such that generally, y = 0 for any optimal solution for fo.

## Slide 21: PRELIMINARY RESULTS
Figure 5: Topology output for the design zone with nelx = 20; nely = 20 and no area and inertial dependency and showing displacements in red
Figure 6: Compliance and volume fraction reduction versus iteration number

## Slide 22: AREA AND INERTIAL INTEGRATION
We take a region close to the truss such that the ‘density’ of the elements in that region determines the average area of cross-section and inertia values for the following iteration of the generation of the stiffness matrix.
Figure 7: Topology output for the design zone with nelx = 20; nely = 20 and with area and inertial dependency showing changes in topology output
Figure 8: Compliance, volume fraction and area reduction versus iteration number

## Slide 23: STATIC CONDENSATION
The goal is to effectively reduce the number of nodes in the truss members. By relating the displacements of one node to the other, the effective number of nodes in the truss members may be thus reduced
Figure 9: Beam truss before condensation
Figure 10: Beam truss after condensation

## Slide 24: MILESTONES
Literature Review on Condensation(Contd.)
Choice of Condensation Modelling Technique
Implementation of Working Code
Time Complexity Comparison
Testing of Code on Sample Cases

## Slide 25: KEY CHALLENGES
Choosing appropriate assumptions for mass distributions in the engine.
Choosing our decision variables carefully so as to not lose out important regions in the structure to optimize.
Building a code that is reasonably fast.
Notes: 1. Choosing appropriate assumptions for mass distributions across the structure in the condensation model to accurately model physics can be a big challenge. If the mass distribution is not appropriately chosen we can get a large variation in the value of natural frequencies and hence dynamic behaviour of structures (20% in some cases [6]).
So, how should we distribute the mass associated with a node to avoid this error?
2. Given that our problem is one on optimization and not condensation, we have to choose our decision variables quite carefully so as to not lose out important regions in the structure to optimize. There mostly exists a trade-off between how well we can condense and how well we can optimize the structure. Which is the minimal number of retained DOFs of beam truss you should keep? Can we improve the classic strategy?
3. The gain in terms of computational cost is quite unclear and may not be as high as one might think if the code has to condense the model every time we run an optimization. Reduction in time complexity of the code remains a mystery. Is our code reasonably fast?

## Slide 26: Thank you! Questions/Suggestions?